## Slide 1: PPG Force Sensor
7/6/2021

## Slide 2: Hypodermal photoplethysmography sensor
Photoplethysmography (PPG) = optical sensing of blood volume changes in microvasculature.
PPG is commonly deployed on wearables: finger clips, smartwatches, etc.
Typically measures oxygen saturation, blood pressure, cardiac output
However, it has also been used to measure fingertip forces noninvasively from fingernail:

## Slide 3: Hypodermal photoplethysmography sensor
Wearable PPG has even been implemented in a wireless, battery free device

## Slide 4: Hypodermal photoplethysmography sensor
Implantable PPG sensors for cardiovascular applications, but not for tactile sensing

## Slide 5: Hypodermal photoplethysmography sensor
Implantable PPG sensor for tactile sensing?
Implement off-the-shelf design of Kim et al 2017, but within fused silica package?

## Slide 6: PPG Sensor: 1st Iteration
Proof-of-concept: Red + IR LED, photodiode
Photodiode
Red LED
IR LED

## Slide 7: PPG Sensor: 2nd Iteration
Added green LED, op-amp to replace resistors
PD not sensitive to green LED light
Force tracked a bit too well in the last one…
  Arduino ADC readings affected each other due to high output impedance of PD circuit => op-amp buffer
Skin contact with wires also led to a falsely increased response
  Might be worth looking into…
  Added clear plastic layer between thumb and sensor
Red LED
Green LED
IR LED
PD
op-amp

## Slide 8: PPG Sensor – Miniaturized PCB
Components:
  ATtiny20 – LED switching, ADC samples photodiode output, sends data to NFC
  NFC chip: receives power, transmits photodiode readings
  Red, IR LED
  Photodiode
Adding Revisions:
  Op Amp buffer?
  Can use smaller PD
  Min Manufacturing size: 5x6 mm => indicators for debugging
Programming
Headers
3.75 mm
4.95 mm